## Slide 1: Headless Pi
Work with a Raspberry Pi from your computer without a monitor, keyboard or mouse attached to the Pi

## Slide 2: Agenda
Preparing
the OS Image
Connecting the FTDI Cable
Booting and Logging In
Configuring the Pi

## Slide 3: Preparing the OS Image
Download the image for the Raspbian OS as a “.zip” from: https://www.raspberrypi.org/downloads/raspbian/
  If you need an older version, checkout: http://downloads.raspberrypi.org/raspbian/images/
  For example, the last version of Raspbian “Jessie” is at: .../images/raspbian-2017-07-05/2017-07-05-raspbian-jessie.zip
Download and install Etcher.io for your platform from https://etcher.io/
Insert the Micro-SD card for the pi into your computer
Use Etcher.io to flash the OS image “.zip” file to the SD card

## Slide 4: Enable the UART on the Pi
With the newly flashed SD card still in your computer
Open the “config.txt” file at the root of the “boot” partition in the text editor of your choice
Add the following two lines to the bottom of the file: # Enable UART enable_uart=1
Save the changes to the “config.txt” file
Safely eject the SD car from your computer
Insert the SD Card into the SD Card slot on the Raspberry Pi

## Slide 5: Get the Cable
https://www.adafruit.com/product/954

## Slide 6: Connect the FTDI cable

## Slide 7: Install the Drivers and Software
Windows: software-installation-windows
Mac: software-installation-mac
Linux: software-installation-linux

## Slide 8: Determine the port for the FTDI Cable
Widows
Open Device Manager
Expand “Ports (COM & LPT)
Identify the Profilic COM Port
macOS / Linux
From a terminal prompt, run ls /dev/cu.*
Locate a device named similar to one of these: /dev/cu.usbserial-NNNN /dev/cu.SLAB_USBtoUART /dev/cu.usbmodem

## Slide 9: Connect using Terminal Software
Windows
PuTTY
macOS / Linux
screen

## Slide 10: Boot the Pi
Ensure the SD Card is in
Ensure the FTDI Cable is connected
Connect Ethernet if Available
Plug in the USB Power Supply
When prompted in the terminal window login: User name: pi Password: raspberry

## Slide 11
Optional Ethernet
Optional WiFi for Pi 2

## Slide 12
Optional Ethernet if desired
Optional WiFi Dongle for Pi 2

## Slide 13: Boot the Pi
Ensure the SD Card is in
Ensure the FTDI Cable is connected
Connect Ethernet if Available
Plug in the USB Power Supply
When prompted in the terminal window login: User name: pi Password: raspberry

## Slide 14: Enable SSH / VNC
sudo raspi-config nonint do_ssh 0
sudo raspi-config nonint do_vnc 0

## Slide 15: Enable Camera, I2C and SPI
Optionally enable the Camera, I2C and SPI Interfaces
sudo raspi-config nonint do_camera 0
sudo raspi-config nonint do_i2c 0
sudo raspi-config nonint do_spi 0
You can alternatively run raspi_config interactively to set these options as well as many others.
sudo raspi-config

## Slide 16: Configure WiFi with wpa_cli
sudo wpa_cli
> set country us (or your country code) > scan > scan_results (find network in list) > add_network (should add network 0) > set_network 0 ssid “your_network_ssid” > set_network 0 psk “your_network_preshared_key” or for an open network set_network 0 key_mgmt NONE > enable_network 0 > save_config > quit sudo cat /etc/wpa_supplicant/wpa_supplicant.conf (verify the config you specified above is written to the file)

## Slide 17: OPTIONAL: Manually edit wpa_supplicant.conf
sudo nano /etc/wpa_supplicant/wpa_supplicant.conf Edit to match the following:
ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev
update_config=1
country=us
network={
ssid=“your_network_ssid"
psk=“your_network_preshared_key"
}

## Slide 18: OPTIONAL: wpa_supplicant.conf for Open newtork
sudo nano /etc/wpa_supplicant/wpa_supplicant.conf Edit to match the following:
ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev
update_config=1
country=us
network={
ssid=“your_network_ssid"
key_mgmt NONE
}

## Slide 19: Manually Cycle the WiFi Interface
sudo ifdown wlan0 sudo ifup wlan0

## Slide 20: Change your hostname
sudo nano /etc/hostname
Change name to something unique
Save the changes
sudo reboot
The pi should be broadcasting its name as “hostname.local” You should be able to ping it with “hostname.local” from your computer to get it’s IP address. (note, on windows, add -4 to your ping command to get it’s IPV4 address):
ping yourpishostname.local -4

## Slide 21: Determine your Pi’s IP addresses
On the pi:
ip -4 a (-4 for IPV4 “a” short of “addr”)
Find Ips in output:
1: lo: <LOOPBACK,UP,LOWER_UP> mtu 65536 qdisc noqueue state UNKNOWN group default qlen 1
inet 127.0.0.1/8 scope host lo
valid_lft forever preferred_lft forever
2: eth0: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc pfifo_fast state UP group default qlen 1000
inet 192.168.2.44/24 brd 192.168.2.255 scope global eth0
valid_lft forever preferred_lft forever
3: wlan0: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc pfifo_fast state UP group default qlen 1000
inet 192.168.2.43/24 brd 192.168.2.255 scope global wlan0
valid_lft forever preferred_lft forever

## Slide 22: Optionally configure ssh keys
Open bash on Windows, and run the following accepting all the defaults (including the empty passkey) ssh-keygen -t rsa -C "SSH Key for logging into the pi“
ssh into the pi with the password, and create the .ssh folder for the pi profile: #RUN THESE COMMANDS ON THE PI cd ~ install -d -m 700 ~/.ssh
Back on your computer, copy they key you created earlier like this, typing in the password one last time: # RUN THIS COMMAND IN BASH ON YOUR WINDOWNS LAPTOP cat ~/.ssh/id_rsa.pub | ssh pi@your.pi.ip.address 'cat >> .ssh/authorized_keys'

## Slide 23: You can now ssh / vnc into the pi

## Slide 24: Install and Configure SAMBA
sudo apt-get update
sudo apt-get upgrade
sudo apt-get install -y samba samba-common-bin
sudo mv /etc/samba/smb.conf /etc/samba/smb.conf.original
sudo nano /etc/samba/smb.conf REPLACE smb.conf file with contents from next slide sudo smbpasswd -a pi From a NON-ADMINISTRATIVE command prompt on your Windows PC, run: net use P: \\your.pi.ip.address\root /user:pi /persistent:yes Now you can open the “P:” drive on your windows pc to see the root of the Pi’s file system

## Slide 25: smb.conf contents
[global] workgroup = WORKGROUP dns proxy = no log file = /var/log/samba/log.%m max log size = 1000 syslog = 0 panic action = /usr/share/samba/panic-action %d server role = standalone server passdb backend = tdbsam obey pam restrictions = yes unix password sync = yes passwd program = /usr/bin/passwd %u passwd chat = *Enter\snew\s*\spassword:* %n\n *Retype\snew\s*\spassword:* %n\n *password\supdated\ssuccessfully* . pam password change = yes map to guest = bad user usershare allow guests = yes [root] comment = root path=/ browseable=YES writeable=YES valid users= pi, root only guest=no create mask=0777 directory mask=07777 public=no force user = root

## Slide 26: Install build tools
sudo apt-get install -y cmake build-essential curl libcurl4-openssl-dev libssl-dev uuid-dev python-dev python-smbus

## Slide 27: Update git and install node 8.x
sudo apt-get install git curl -sL https://deb.nodesource.com/setup_8.x | sudo -E bash -
sudo apt-get install -y nodejs

## Slide 28: Upgrade pip to v9
python -m pip install --upgrade pip

## Slide 29: Install Azure IoT Device SDK for Python
pip install azure-iothub-device-client
https://github.com/Azure/azure-iot-sdk-python/blob/master/doc/python-devbox-setup.md#windows-wheels

## Slide 30: Build the Azure IoT Hub SDK for Python
YOU SHOULDN’T HAVE TO DO THIS
At a terminal prompt on the pi:
sudo apt-get install -y cmake build-essential curl libcurl4-openssl-dev libssl-dev uuid-dev python-dev python-smbus
cmake --version # (ensure version is at least 2.8.12)
gcc --version # (ensure version is at least 4.4.7)
python --version # (ensure 2.7, 3.4 or 3.5, note it for use below)
sudo apt-get update
cd ~
git clone https://github.com/Azure/azure-iot-sdk-python.git --recursive
cd azure-iot-sdk-python/build_all/linux
./setup.sh --python-version 2.7 # Replace the 2.7 with 3.4 or 3.5 as desired. Takes 2+ minutes depending on network speed
./build.sh --build-python 2.7 # Replace the 2.7 with 3.4 or 3.5 as desired. Takes 10-11+ minutes
# copy ~/azure-iot-sdk-python/device/samples/iothub_client.so to your python app folder for use.

## Slide 31: Config SPI
sudo modprobe spi-bcm2835
# Ensure SPI and I3C are enabled if you didn’t do so previously
sudo raspi-config nonint do_ssh 0
sudo raspi-config nonint do_vnc 0
# Install BCM driver for python
sudo modprobe spi-bcm2835
sudo apt-get update
sudo apt-get upgrade
sudo apt-get install python-dev python3-dev
cd ~
git clone https://github.com/doceme/py-spidev.git
cd py-spidev
make
sudo make install

## Slide 32: Do a demo!

## Slide 33
AZURE
INGENU
FIELD
Ingenu RPMA Access Point
Ingenu Intellect Platform - REST or AMQP
Resource Group <name>group
App Service Plan ingenuplan
Function App ingenufunctions
Storage Account ingenustorage
Function IntellectRest2IoTHubJs
IoT Hub ingenuhub
Stream Analytics Job ingenujob
SQL Server ingenusql
SQL Database
ingenudb
Service Bus Namespace ingenubus
Event Hub
ingenualerts
Web App ingenuweb
Power BI Embedded Collection ingenucollection
Power BI Embedded Workspace Dynamic GUID
Power BI Report Temperature Chart
Function EventHub2IntellectRestJS
UPLINK
BACKHAUL
GET
SEND
READ/WRITE
INPUT
OUTPUT
OUTPUT
QUERY
GET
QUERY
RENDER
RECEIVE
POST
DOWNLINK
RPMA to Azure
Architecture Diagram

## Slide 35: IoT Logo

## Slide 36: arduino

## Slide 37: Arduino 101

## Slide 38: Grove Base Shield

## Slide 39: Grove cable & SENSORS

## Slide 40: Grove cable & SENSORS

## Slide 41: INTEL NUC DE3815TYKE

## Slide 42: GALILEO BOARD

## Slide 43: Raspberry Pi 3 PNG
https://commons.wikimedia.org/wiki/File:Raspberry_Pi_3_illustration.svg

## Slide 44: RASPBERRY PI

## Slide 47: FEZ SPIDER MAIN BOARD

## Slide 48: Sparkfun weather shield

## Slide 49: FEZ HAT

## Slide 50: Device graphics from docs
Device with Filled Holes
Device with Through Holes
This is a version of the Device icon used in the “Extended IoT Scenarios” in docs. For example: https://docs.microsoft.com/en-us/azure/iot-hub/iot-hub-explorer-cloud-device-messaging

## Slide 51: Connect the dots azure icons
Microsoft Azure
Event Hubs
Stream Analytics
Storage blob
Storage table
SQL database
(
generic
)
Storage
(
Azure
)
Web App
Machine
Learning
GitHub code
Git repository
Service Bus
HDInsight

## Slide 52: cables

## Slide 53: More cables and adapters

## Slide 54: LEDs
Long Leg
Short Leg
Small Post
Big Post
Flat Edge
Vcc (+)
GND
Anode (+)
Cathode (-)

## Slide 55: LEDs

## Slide 56: Current limiting resistors
Providing more current than an LED is rated for can destroy the LED. To prevent that, you should use a “Current Limiting” resistor.
To calculate the value of the resistor you need to know the supply voltage (Usually 5V on the Arduino Uno), and the LEDs rated Forward Voltage (the voltage drop across the LED) and Forward Current (the maximum current the LED can handle).
The Arduino Uno has a built in current limiting resistor on Pin 13. If you use Pin 13 to power your LED you can use it without a separate resistor.

## Slide 57: Resistors
1st Digit
2nd Digit
Multiplier
Tolerance
Color | Name | 1st Digit | 2nd Digit | Multiplier | Tolerance
 | Black | 0 | 0 | X1 | 
 | Brown | 1 | 1 | X10 | 1%
 | Red | 2 | 2 | X100 | 
 | Orange | 3 | 3 | X1,000 | 
 | Yellow | 4 | 4 | X10,000 | 
 | Green | 5 | 5 | X100,000 | 
 | Blue | 6 | 6 | X1,000,000 | 
 | Violet | 7 | 7 |  | 
 | Grey | 8 | 8 |  | 
 | White | 9 | 9 |  | 
 | Gold |  |  | X0.1 | 5%
 | Silver |  |  | X0.01 | 10%
220Ω
330Ω
10KΩ

## Slide 58: Potentiometer – variable resistor

## Slide 59: breadboards
Breadboards offer a great way to prototype circuits. The provide a number of “buses” for connecting both power and components.
Power buses run the entire horizontal length
Component buses give you easy ways to connect pins together

## Slide 62: Micro SD Cards
Font: Segoe UI Semibold