## Slide 1: Headless Pi
Work with a Raspberry Pi from your computer without a monitor, keyboard or mouse attached to the Pi

## Slide 2: Agenda
Preparing
the OS Image
Connecting the FTDI Cable
Booting and Logging In
Configuring the Pi

## Slide 3: Preparing the OS Image
Download the image for the Raspbian OS as a “.zip” from: https://www.raspberrypi.org/downloads/raspbian/
  If you need an older version, checkout: http://downloads.raspberrypi.org/raspbian/images/
  For example, the last version of Raspbian “Jessie” is at: .../images/raspbian-2017-07-05/2017-07-05-raspbian-jessie.zip
Download and install Etcher.io for your platform from https://etcher.io/
Insert the Micro-SD card for the pi into your computer
Use Etcher.io to flash the OS image “.zip” file to the SD card

## Slide 4: Enable the UART on the Pi
With the newly flashed SD card still in your computer
Open the “config.txt” file at the root of the “boot” partition in the text editor of your choice
Add the following two lines to the bottom of the file: # Enable UART enable_uart=1
Save the changes to the “config.txt” file
Safely eject the SD car from your computer
Insert the SD Card into the SD Card slot on the Raspberry Pi

## Slide 5: Get the Cable
https://www.adafruit.com/product/954

## Slide 6: Connect the FTDI cable

## Slide 7: Install the Drivers and Software
Windows: software-installation-windows
Mac: software-installation-mac
Linux: software-installation-linux

## Slide 8: Determine the port for the FTDI Cable
Widows
Open Device Manager
Expand “Ports (COM & LPT)
Identify the Profilic COM Port
macOS / Linux
From a terminal prompt, run ls /dev/cu.*
Locate a device named similar to one of these: /dev/cu.usbserial-NNNN /dev/cu.SLAB_USBtoUART /dev/cu.usbmodem

## Slide 9: Connect using Terminal Software
Windows
PuTTY
macOS / Linux
screen

## Slide 10: Boot the Pi
Ensure the SD Card is in
Ensure the FTDI Cable is connected
Connect Ethernet if Available
Plug in the USB Power Supply
When prompted in the terminal window login: User name: pi Password: raspberry

## Slide 11: Boot the Pi
Ensure the SD Card is in
Ensure the FTDI Cable is connected
Connect Ethernet if Available
Plug in the USB Power Supply
When prompted in the terminal window login: User name: pi Password: raspberry

## Slide 12: Enable SSH / VNC
sudo raspi-config nonint do_ssh 0
sudo raspi-config nonint do_vnc 0
Optionally enable the Camera, I2C and SPI Interfaces
sudo raspi-config nonint do_camera 0
sudo raspi-config nonint do_i2c 0
sudo raspi-config nonint do_spi 0

## Slide 13: Enable Camera, I2C and SPI
sudo raspi-config nonint do_camera 0
sudo raspi-config nonint do_i2c 0
sudo raspi-config nonint do_spi 0

## Slide 14: Configure WiFi with wpa_cli
sudo wpa_cli
> set country us (or your country code) > scan > scan_results (find network in list) > add_network (should add network 0) > set_network 0 ssid “your_network_ssid” > set_network 0 psk “your_network_preshared_key” or for an open network set_network 0 key_mgmt NONE > enable_network 0 > save_config > quit sudo cat /etc/wpa_supplicant/wpa_supplicant.conf (verify the config you specified above is written to the file)

## Slide 15: Manually edit wpa_supplicant.conf
sudo nano /etc/wpa_supplicant/wpa_supplicant.conf Edit to match the following:
ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev
update_config=1
country=us
network={
ssid=“your_network_ssid"
psk=“your_network_preshared_key"
}

## Slide 16: Open network wpa_supplicant.conf
sudo nano /etc/wpa_supplicant/wpa_supplicant.conf Edit to match the following:
ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev
update_config=1
country=us
network={
ssid=“your_network_ssid"
key_mgmt NONE
}

## Slide 17: Change your hostname
sudo nano /etc/hostname
Change name to something unique
Save the changes
sudo reboot
The pi should be broadcasting its name as “hostname.local” You should be able to ping it with “hostname.local” from your computer to get it’s IP address. (note, on windows, add -4 to your ping command to get it’s IPV4 address):
ping yourpishostname.local -4

## Slide 18: Determine your Pi’s IP addresses
On the pi:
ip -4 a (-4 for IPV4 “a” short of “addr”)
Find Ips in output:
1: lo: <LOOPBACK,UP,LOWER_UP> mtu 65536 qdisc noqueue state UNKNOWN group default qlen 1
inet 127.0.0.1/8 scope host lo
valid_lft forever preferred_lft forever
2: eth0: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc pfifo_fast state UP group default qlen 1000
inet 192.168.2.44/24 brd 192.168.2.255 scope global eth0
valid_lft forever preferred_lft forever
3: wlan0: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc pfifo_fast state UP group default qlen 1000
inet 192.168.2.43/24 brd 192.168.2.255 scope global wlan0
valid_lft forever preferred_lft forever

## Slide 19: Optionally configure ssh keys
Open bash on Windows, and run the following accepting all the defaults (including the empty passkey) ssh-keygen -t rsa -C "SSH Key for logging into the pi“
ssh into the pi with the password, and create the .ssh folder for the pi profile: #RUN THESE COMMANDS ON THE PI cd ~ install -d -m 700 ~/.ssh
Back on your computer, copy they key you created earlier like this, typing in the password one last time: # RUN THIS COMMAND IN BASH ON YOUR WINDOWNS LAPTOP cat ~/.ssh/id_rsa.pub | ssh pi@your.pi.ip.address 'cat >> .ssh/authorized_keys'

## Slide 20: You can now ssh / vnc into the pi

## Slide 21: Install and Configure SAMBA
sudo apt-get update
sudo apt-get upgrade
sudo apt-get install -y samba samba-common-bin
sudo mv /etc/samba/smb.conf /etc/samba/smb.conf.original
sudo nano /etc/samba/smb.conf REPLACE smb.conf file with contents from next slide sudo smbpasswd -a pi From a NON-ADMINISTRATIVE command prompt on your Windows PC, run: net use P: \\your.pi.ip.address\root /user:pi /persistent:yes Now you can open the “P:” drive on your windows pc to see the root of the Pi’s file system

## Slide 22: smb.conf contents
[global] workgroup = WORKGROUP dns proxy = no log file = /var/log/samba/log.%m max log size = 1000 syslog = 0 panic action = /usr/share/samba/panic-action %d server role = standalone server passdb backend = tdbsam obey pam restrictions = yes unix password sync = yes passwd program = /usr/bin/passwd %u passwd chat = *Enter\snew\s*\spassword:* %n\n *Retype\snew\s*\spassword:* %n\n *password\supdated\ssuccessfully* . pam password change = yes map to guest = bad user usershare allow guests = yes [root] comment = root path=/ browseable=YES writeable=YES valid users= pi, root only guest=no create mask=0777 directory mask=07777 public=no force user = root

## Slide 23: Install build tools
sudo apt-get install -y cmake build-essential curl libcurl4-openssl-dev libssl-dev uuid-dev python-dev python-smbus

## Slide 24: Update git and install node 8.x
sudo apt-get install git curl -sL https://deb.nodesource.com/setup_8.x | sudo -E bash -
sudo apt-get install -y nodejs

## Slide 25: Build the Azure IoT Hub SDK for Python
At a terminal prompt on the pi:
sudo apt-get install -y cmake build-essential curl libcurl4-openssl-dev libssl-dev uuid-dev python-dev python-smbus
cmake --version # (ensure version is at least 2.8.12)
gcc --version # (ensure version is at least 4.4.7)
python --version # (ensure 2.7, 3.4 or 3.5, note it for use below)
sudo apt-get update
cd ~
git clone https://github.com/Azure/azure-iot-sdk-python.git --recursive
cd azure-iot-sdk-python/build_all/linux
./setup.sh --python-version 2.7 # Replace the 2.7 with 3.4 or 3.5 as desired. Takes 2+ minutes depending on network speed
./build.sh --build-python 2.7 # Replace the 2.7 with 3.4 or 3.5 as desired. Takes 10-11+ minutes
# copy ~/azure-iot-sdk-python/device/samples/iothub_client.so to your python app folder for use.

## Slide 26: Do a demo!

## Slide 27
AZURE
INGENU
FIELD
Ingenu RPMA Access Point
Ingenu Intellect Platform - REST or AMQP
Resource Group <name>group
App Service Plan ingenuplan
Function App ingenufunctions
Storage Account ingenustorage
Function IntellectRest2IoTHubJs
IoT Hub ingenuhub
Stream Analytics Job ingenujob
SQL Server ingenusql
SQL Database
ingenudb
Service Bus Namespace ingenubus
Event Hub
ingenualerts
Web App ingenuweb
Power BI Embedded Collection ingenucollection
Power BI Embedded Workspace Dynamic GUID
Power BI Report Temperature Chart
Function EventHub2IntellectRestJS
UPLINK
BACKHAUL
GET
SEND
READ/WRITE
INPUT
OUTPUT
OUTPUT
QUERY
GET
QUERY
RENDER
RECEIVE
POST
DOWNLINK
RPMA to Azure
Architecture Diagram

## Slide 29: IoT Logo

## Slide 30: arduino

## Slide 31: Arduino 101

## Slide 32: Grove Base Shield

## Slide 33: Grove cable & SENSORS

## Slide 34: Grove cable & SENSORS

## Slide 35: INTEL NUC DE3815TYKE

## Slide 36: GALILEO BOARD

## Slide 37: Raspberry Pi 3 PNG
https://commons.wikimedia.org/wiki/File:Raspberry_Pi_3_illustration.svg

## Slide 38: RASPBERRY PI

## Slide 41: FEZ SPIDER MAIN BOARD

## Slide 42: Sparkfun weather shield

## Slide 43: FEZ HAT

## Slide 44: Device graphics from docs
Device with Filled Holes
Device with Through Holes
This is a version of the Device icon used in the “Extended IoT Scenarios” in docs. For example: https://docs.microsoft.com/en-us/azure/iot-hub/iot-hub-explorer-cloud-device-messaging

## Slide 45: Connect the dots azure icons
Microsoft Azure
Event Hubs
Stream Analytics
Storage blob
Storage table
SQL database
(
generic
)
Storage
(
Azure
)
Web App
Machine
Learning
GitHub code
Git repository
Service Bus
HDInsight

## Slide 46: cables

## Slide 47: More cables and adapters

## Slide 48: LEDs
Long Leg
Short Leg
Small Post
Big Post
Flat Edge
Vcc (+)
GND
Anode (+)
Cathode (-)

## Slide 49: LEDs

## Slide 50: Current limiting resistors
Providing more current than an LED is rated for can destroy the LED. To prevent that, you should use a “Current Limiting” resistor.
To calculate the value of the resistor you need to know the supply voltage (Usually 5V on the Arduino Uno), and the LEDs rated Forward Voltage (the voltage drop across the LED) and Forward Current (the maximum current the LED can handle).
The Arduino Uno has a built in current limiting resistor on Pin 13. If you use Pin 13 to power your LED you can use it without a separate resistor.

## Slide 51: Resistors
1st Digit
2nd Digit
Multiplier
Tolerance
Color | Name | 1st Digit | 2nd Digit | Multiplier | Tolerance
 | Black | 0 | 0 | X1 | 
 | Brown | 1 | 1 | X10 | 1%
 | Red | 2 | 2 | X100 | 
 | Orange | 3 | 3 | X1,000 | 
 | Yellow | 4 | 4 | X10,000 | 
 | Green | 5 | 5 | X100,000 | 
 | Blue | 6 | 6 | X1,000,000 | 
 | Violet | 7 | 7 |  | 
 | Grey | 8 | 8 |  | 
 | White | 9 | 9 |  | 
 | Gold |  |  | X0.1 | 5%
 | Silver |  |  | X0.01 | 10%
220Ω
330Ω
10KΩ

## Slide 52: Potentiometer – variable resistor

## Slide 53: breadboards
Breadboards offer a great way to prototype circuits. The provide a number of “buses” for connecting both power and components.
Power buses run the entire horizontal length
Component buses give you easy ways to connect pins together

## Slide 56: Micro SD Cards
Font: Segoe UI Semibold